## Slide 1
SEPTEMBER 2026 BRIEFING
Sonardyne
in Brazil
Pre-salt projects, partners and new technology
On Demand Ocean Bottom Nodes at Mero, optical data harvesting and the fleet behind Brazil's deepwater operations
Based on trade press and company news to September 2026
Notes: Deck summarises Sonardyne's Brazil activity from trade press and company sources: Offshore Magazine, JPT, Marine Technology News, Kraken Robotics releases and Sonardyne news.

## Slide 2
AT A GLANCE
Three things to know
Sonardyne in Brazil
02 / 12
20+
years in Brazil
Local office, in-country support and Portuguese-speaking engineers since the 2000s
84
OD OBNs at Mero
First field deployment of On Demand Ocean Bottom Nodes, early 2026
2027
commercial production
Scale-up could mean hundreds or thousands of nodes per field
Notes: Executive summary. Sonardyne has had a local presence in Brazil for more than 20 years; the flagship OD OBN programme reached its first field deployment at the Petrobras-operated Mero field in early 2026; Kraken Robotics expects commercial production from 2027.

## Slide 3
OUR HISTORY
Two decades on the ground built today's trust
Sonardyne in Brazil
03 / 12
2015
Second office opens in central Rio, alongside the Rio das Ostras base
2016
Ranger 2 + GyroUSBL 7000 on Fugro Aquarius for Petrobras ROV work to 3,000 m
2018
OD OBN programme starts with Shell, Petrobras and SENAI CIMATEC
2020
Orders from OceanPact and C-Innovation (six vessels)
2025
OD OBN final tests after 2,000+ days of deepwater trials
2026
First 84 OD OBNs deployed at Mero
Portuguese-speaking support staff are a key reason operators stay with Sonardyne.
C-Innovation, 2022 case study. Sonardyne Brasil Ltda kept its office open through downturns and COVID-19.
Notes: Office details from Sonardyne's May 2015 release. C-Innovation case study published October 2022. Mero deployment reported by JPT (June 2026) and Kraken Robotics (July 2026). Sonardyne Brasil Ltda provides in-country technical support, repair, training and sales.

## Slide 4
ECOSYSTEM
Operators, researchers and vessel owners
Sonardyne in Brazil
04 / 12
Operators
Petrobras
Mero operator; R&D via CENPES
Shell Brasil
Co-leads OD OBN; 19.3% of Mero
Karoon Energy
Client for C-Innovation's Cabo Frio
Research & funding
SENAI CIMATEC
Co-manufactures nodes at Camaçari
ANP
Regulator; funds OD OBN via R&D clause
Saipem
FlatFish AUV harvests node data
Vessel operators
C-Innovation
ROV/IMR fleet: Ranger 2, SPRINT-Nav, Fusion 2
Fugro
Fugro Aquarius: Ranger 2 + GyroUSBL 7000
OceanPact
Ranger 2 on geoscience vessels for Petrobras
Notes: Petrobras: operator of Mero, R&D via CENPES, and client on Fugro and OceanPact charters. SENAI CIMATEC co-manufactures nodes at Camaçari and runs deployments. C-Innovation (Edison Chouest affiliate) also serves Shell, Chevron, ExxonMobil, BP and PetroRio in Brazil, according to Sonardyne's 2022 case study; its fleet using Sonardyne grew from 2 to 15 vessels.

## Slide 5
FLAGSHIP PROJECT
OD OBN: 4D monitoring without node recovery
Sonardyne in Brazil
05 / 12
Semi-permanent seabed seismic nodes for low-cost 4D reservoir monitoring of the pre-salt
2,000+
days of deepwater trials at Sapinhoá, Itapu and Búzios
660
pre-production nodes in the pilot array
84
nodes in the first Mero deployment, early 2026
5 yrs
design life on the seabed, rated to 3,000 m
WHY IT MATTERS
No repeat deployment and recovery: data is harvested wirelessly, on demand
Lower greenhouse-gas emissions from seismic acquisition and more offshore automation (Petrobras CENPES)
Notes: Figures: Offshore Magazine (Jan 2026), Marine Technology News, JPT (June 2026). Node life of up to five years and 3,000 m depth rating per JPT. Some sources give the pilot array as 600 nodes (2024 plan) and later 660 (2026).

## Slide 6
HOW IT WORKS
Acoustics to control, optics to collect
Sonardyne in Brazil
06 / 12
Survey vessel
Acoustic command + clock sync
OD OBNs on the seabed, ~2,000 m
FlatFish AUV
BlueComm optical download
1 Deploy
Nodes left over the reservoir for years
2 Sync
Acoustic commands start recording and sync clocks
3 Record
Capture energy reflected from the reservoir
4 Harvest
AUV pulls data over a BlueComm optical link
5 Process
4D workflows track fluid movement
Notes: Two links, two jobs: acoustics for long-range control and timing; optics for short-range, high-volume data transfer. The data harvesting vehicle is Saipem's FlatFish AUV, with ROV retrieval as an alternative (Sonardyne case study). Results are used to adjust extraction rates and fluid reinjection (JPT). Schematic is illustrative, not to scale.

## Slide 7
FIRST FIELD DEPLOYMENT
Mero: first field deployment in the pre-salt
Sonardyne in Brazil
07 / 12
Mero consortium share
Chart: 
| Petrobras | Shell Brasil | TotalEnergies | CNPC | CNOOC | PPSA
Share | 38.6 | 19.3 | 19.3 | 9.65 | 9.65 | 3.5
38.6%
Petrobras
Petrobras 38.6%
Shell Brasil 19.3%
TotalEnergies 19.3%
CNPC 9.65%
CNOOC 9.65%
PPSA 3.5%
Santos Basin pre-salt, ~2,000 m water depth
First 84 nodes of the pilot batch placed early 2026
Commercial production expected 2027
“Seeing the OD OBN system successfully deployed at Mero is a strong validation of the technology and the collaborative R&D behind it.”
Shaun Dunn, Sonardyne (JPT, June 2026)
Notes: Next steps: seismic acquisition over the monitored area, optical data retrieval, 4D processing and assessment of reservoir-management value. Shell Brasil's Manoela Lopes called the Mero deployment a decisive step in maturing the technology.

## Slide 8
TECHNOLOGY
Four building blocks behind the programme
Sonardyne in Brazil
08 / 12
BlueComm optical comms
2.5–10 Mbps
up to 75 m; rated to 4,000 m. 9 GB+ moved on one lithium D-cell
Wideband acoustic control
100s of nodes
Long-range commands and seismic-grade clock sync, from 6G heritage
Resident AUV harvesting
No recovery
Saipem FlatFish collects data wirelessly; ROV retrieval as fallback
Made in Brazil
600 / year
Planned capacity at CIMATEC PARK, Camaçari, Bahia
Notes: Press coverage names BlueComm as the optical system but does not state which model the nodes use; the BlueComm 200 UV figures are Sonardyne's current product specs. Sonardyne leads communications, integration and co-manufacturing. Plant capacity of 600 nodes a year is from the 2024 announcement.

## Slide 9
VESSEL POSITIONING
Positioning Brazil's deepwater fleet
Sonardyne in Brazil
09 / 12
Ranger 2 USBL
C-Innovation, Fugro, OceanPact
Tracks ROVs, corers and towed sensors; DP reference
GyroUSBL 7000
Fugro Aquarius
Transceiver + survey-grade INS in one unit, to 3,000 m
SPRINT-Nav
C-Innovation
Pre-calibrated INS, DVL and depth; cuts ROV set-up time
Fusion 2 LBL
C-Innovation
Real-time SLAM calibration; fewer Compatts to deploy
THE BENCHMARK
< 5 m
error at 1,000 m water depth
95% of positions within 0.5% of water depth, while the vessel is moving
Notes: C-Innovation's Sonardyne-equipped fleet in Brazil grew from 2 to 15 vessels (2022 case study). Its 2020 order covered SPRINT, Lodestar AHRS, Syrinx DVL, SPRINT-Nav, Compatt 6+ and WSM 6+ for six vessels working for Petrobras and Karoon.

## Slide 10
ROADMAP
What comes next
Sonardyne in Brazil
10 / 12
NOW
Survey & retrieve
Seismic shoot over Mero, then optical data recovery from the nodes
NEXT
Prove the value
4D processing and assessment of how the data supports reservoir management
2027+
Scale up
Commercial production from 2027; full fields may need hundreds or thousands of nodes
CONTEXT
Kraken ownership
Sonardyne joined Kraken Robotics with the Covelya acquisition on 2 July 2026
Notes: Commercial production timing and scale from Kraken Robotics' 20 July 2026 business update.

## Slide 11
KEY TAKEAWAYS
Brazil is where next-generation seabed monitoring goes live
01
Local presence and Portuguese-speaking support underpin long-term operator relationships
02
OD OBN has moved from 2,000+ days of trials to a live deployment at Mero
03
Acoustic control and optical harvesting make repeat 4D surveys cheaper and lower-emission
Notes: Closing summary. Invite questions on the Mero timeline, the scale-up to commercial production from 2027, and what Kraken Robotics ownership means for the Brazil business.

## Slide 12
REFERENCES
Sources
Sonardyne in Brazil
12 / 12
JPT (SPE), 19 June 2026: New seismic acquisition technology advances offshore Brazil
Kraken Robotics, 20 July 2026: $35 million in new orders and business update
Offshore Magazine, 15 Jan 2026: On-demand OBN system enhances surveillance of Brazil's presalt fields
Marine Technology News: On-Demand Ocean Bottom Node, a new era in deepwater seismic monitoring
Sonardyne: OD OBN case study; OD OBN phase release (June 2024); C-Innovation case study (Oct 2022); OceanPact release (June 2020); second Brazil office (May 2015); BlueComm 200 UV product page
Offshore Magazine, Sept 2016: Sonardyne delivers subsea technology to Fugro vessel offshore Brazil
Keyfacts Energy, Oct 2020: C-Innovation selects Sonardyne technology
Node counts differ between sources over time (600 planned in 2024; 660 in production in 2026).